## Slide 1
NVDIMM Internals And
Data Center Workload Profile
Intel AIPG/SSP
fan.du@intel.com
fengguang.wu@intel.com

## Slide 2
Outline
NVDIMM Basics
Data Center Workload Profile

## Slide 3: Intel® Optane™ DC Persistent Memory - Product Overview
IMC
Cascade Lake
IMC
DIMM Capacity
128, 256, 512GB
Speed
2666 MT/sec
Capacity per CPU
3TB (not including DRAM)
Non-Volatile Memory Pool
DDR4 DRAM*
DCPMM*
App Direct
Storage
Memory
DDR4 electrical & physical
Close to DRAM latency
Cache line size access
DRAM, or
DRAM as cache
* DIMM population shown as an example only.
1
MEMORY mode
Storage over APP DIRECT
● Large memory at lower cost
● Low latency persistent memory
● Fast direct-attach storage
● Persistent data for rapid recovery
2
APP DIRECT mode

## Slide 4
OS transparent Usage
HW 2LM (Memory Mode)
OS transparent
OS visible size: DCPMM size
Memory Mode
(MM)
DRAM
Cache
DCPMM
Volatile
Memory Mode
(2nd Level Memory)
Volatile with DRAM caching

## Slide 5
OS Visible Usage - App Direct Interfaces
Block Device /dev/pmemX.Y
Char Device /dev/daxX.Y
Memory only NUMA node

## Slide 6: Heterogeneous Memory Tiering Ideas
Question:
How to know workload fit best to what types of memory beforehand?
Heterogeneous memory solutions:
Software-Defined Far Memory in Warehouse-Scale Computers Paper
HMEM: https://lkml.org/lkml/2019/10/16/1187
https://arxiv.org/abs/1907.12014
HBM
DRAM
NVDIMM(DCPMM)
  Memory mode
  NUMA node

## Slide 7
Outline
NVDIMM Basics
Data Center Workload Profile

## Slide 8: DCPMM Profiling Tool - Why
Customer puzzles
  Shall I use Intel DCPMM for my workload? => good performance (per $)?
  If yes, how much AEP to be deployed? => best DRAM:AEP ratio?
Fix chicken-and-egg problem by providing a measuring tool
  Run everywhere in legacy customer environment
  Measure online get real characteristics
  Generate reports that help make Intel DCPMM deployment decision

## Slide 9: DCPMM Profiling Tool - Metrics
Memory Bandwidth
  Idle, or
  Low read/write BW, esp. write BW, or
  Lots of cold pages that meet (2)
Memory Capacity
  Large, or
  Large comparing to BW, or
  Large percent of cold pages
Memory Latency
  Not sensitive
App specific
Not auto detectable
need hotness
scan & migration
Just put task in AEP

## Slide 10: DCPMM Profiling Tool - Report contents
Task metrics | value | threshold
Total BW | MB/s | -
Read%, Write% | % | 
Seq%, Rnd% | % | 
BW-per-GB histogram | plot distribution curve and the threshold line | -
Cold pages BW | MB/s | -
Cold BW percent | % | Customer defined, if latency sensitive
Cold pages percent | % | > System AEP% e.g. > 50-80%
Hot drift rate | %/minute | < 5% AEP BW on added costs e.g. < 1%/minute
IPC: insn per cycle local vs remote DRAM | % dropped | 

## Slide 11: DCPMM Profiling Tool - Methodology

## Slide 12: Task Bandwidth Distribution
Chart: 
MB/s per GB | 169.46 | 115.93 | 86.52 | 70.16 | 58.36 | 47.4 | 37.76 | 31.95 | 26.14 | 20.67 | 15.15 | 11.5 | 8.1 | 5.33 | 3.14 | 1.66 | 0.59 | 0.13 | 0.02 | 1.2
X axis: RefCount 19 => 0
 | hot | cold
size | 25% | 75%
bandwidth | 89.6% | 10.4%
Test: sysbench random reads in Gaussian distribution
Reference AEP MB-per-GB

## Slide 13: DCPMM Profiling Tool – Sample Log

## Slide 14: Recap
NVDIMM basics
How to get insights of workload in tiered memory
Source Code:
https://github.com/intel/memory-optimizer/blob/master/profile_tool/README

## Slide 15
Legal Information
INFORMATION IN THIS DOCUMENT IS PROVIDED IN CONNECTION WITH INTEL® PRODUCTS. EXCEPT AS PROVIDED IN INTEL'S TERMS AND CONDITIONS OF SALE FOR SUCH PRODUCTS, INTEL ASSUMES NO LIABILITY WHATSOEVER, AND INTEL DISCLAIMS ANY EXPRESS OR IMPLIED WARRANTY RELATING TO SALE AND/OR USE OF INTEL PRODUCTS, INCLUDING LIABILITY OR WARRANTIES RELATING TO FITNESS FOR A PARTICULAR PURPOSE, MERCHANTABILITY, OR INFRINGEMENT OF ANY PATENT, COPYRIGHT, OR OTHER INTELLECTUAL PROPERTY RIGHT.
Intel may make changes to specifications, product descriptions, and plans at any time, without notice.
All dates provided are subject to change without notice.
Intel is a trademark of Intel Corporation in the U.S. and other countries.
*Other names and brands may be claimed as the property of others.
Copyright © 2007, Intel Corporation. All rights are protected.